## Slide 1: 19CSE211 Computer Architecture & Organization
MIPS-Remaining Portions

## Slide 2: Compiling Loop Statements
C Code
while(save[i]==k) i+=1;
I in $s3, k in $s5, address of save in $s6.
Compiled MIPS code
Loop: sll $t1, $s3, 2
add $t1,$t1,$s6
lw $t0, 0($t1)
bne $t0, $s5, Exit
addi $s3, $s3,1
j Loop
Exit:

## Slide 3: More about Branch Instructions
We have beq, bne but what about other kind of branches(e.g. branch if less than)? For this we need another instruction, slt.
Set on less than instruction:
slt $t0,$s0,$s1 #if $s0<$s1 then
# $t0=1 else
# $t0=0
Instruction Format(R Format)
Alternate Variants of slt
slti $t0, $s0,25 # if $s0<25, then $to=1…..
sltu $t0,$s0,$s1 #if $s0<$s1 then $t0=1….
sltiu $t0,$s0,$s1 #if $s0<$s1 then $t0=1….

## Slide 4: Signed vs Unsigned
Signed comparison: slt,slti
Unsigned comparison: sltu,sltui
Example
$s0=1111 1111 1111 1111 1111 1111 1111 1111
$s1=0000 0000 0000 0000 0000 0000 0000 0001
slt $t0,$s0,$s1 # Signed
-1<+1$t0=1
sltu $t0,$s0,$s1 # Unsigned
+4,294,967,295> +1=> $to=0

## Slide 5: Aside: More Branch Instructions
Can use slt, beq, bne and the fixed value of 0 in $zero to create other conditions.
Less than blt $s1,$s2, Label
slt $at, $s1,$s2 # $at set to 1 if
bne $at, $zero ,Label # $s1<$s2
Less than or equal to ble $s1,$s2, Label
greater than bgt $s1,$s2, label
Greater than or equal to bge $s1,$s2, label

## Slide 6: Branch Instruction Design
Why not include blt,bge etc in the MIPS ISA?
Hardware for <,<=,>..etc slower than = or !=
Combining with branch involves more work per
instruction, requiring a slower clock.
All Instructions will be penalized.
beq and bne are the common case.
This is a good design compromise.

## Slide 7
MIPS Register File(It is a set of registers)
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
locations
32
5
32
5
5
32
Holds thirty-two 32-bit registers
  Two read ports and
  One write port
Registers are
  Faster than main memory
write control
Notes: All machines (since 1975) have used general purpose registers

## Slide 8
We'd also like to be able to load a 32-bit constant into a register, for this we must use two instructions
a new "load upper immediate" instruction
lui $t0, 1010101010101010
Then must get the lower order bits right, use ori $t0, $t0, 1010101010101010
Aside: How About Larger Constants?
16 0 8 10101010101010102
1010101010101010
0000000000000000
1010101010101010
0000000000000000
1010101010101010 1010101010101010
Notes: For lecture
sets the upper 16 bits of a constant in a register, allowing the next instruction to specify the lower 16 bits of the constant
note that lui fills the lower 16 bits of the register with zero’s
why can’t addi be used as the second instruction for this 32 bit constant?
also note – the assembler lets me specify constants larger than 16 bits in one instruction and then expands the code into two instructions (lui and ori) automatically