## Slide 1: 19CSE211:-Computer Organization & Architecture CPU Performance Analysis

## Slide 2: Definition of Performance
For some program running on machine X,
PerformanceX =1/(ExecutionTime)X
Performance X>performance Y
1/Execution Time x>1/Execution Time Y
Execution Time Y > Execution time x
“ X is n times faster than Y”
PerformanceX /PerformanceY = n
Problem
Machine A runs a program in 20 seconds
Machine B runs the same program in 25 seconds.
How much faster is A than B? 25/20

## Slide 3: Performance Factors
CPU Execution Time(CPU Time)-Time the CPU spends working on a task.
It does not include waiting for I/O or running other programs
CPU Execution Time = # CPU Clock Cycles * Clock Cycle Time
for a Program
CPU Execution Time = # CPU Clock Cycles / Clock Rate
for a Program
Can improve performance by reducing either the length of the clock cycles or number of clock cycles required for a program.

## Slide 4: Clock Cycles
Instead of reporting execution time in seconds, we often use clock cycles
So if we want to improve performance, you can either make the clock cycle time less ie seconds/cycle or you can make the number of cycles in a program less. Both of this will result in a faster program.
So to improve performance, (everything else being equal),you can either increase or decrease??
No of required cycles for a program - decrease
clock cycle time means time for a cycle, or said another way-decrease
The clock rate – increase.

## Slide 5: Processor Metrics
The term clock cycles per instruction , which is the average number of clock cycles each instruction takes to execute, is often abbreviated as CPI.
Execution Time= X CPI X Clock Cycle Time
CPI tells us about the ISA and its Implementation

## Slide 6: A given program…
A given program will contain:
  Some number of instructions(at the machine level)
  Some number of cycles
  Some number of seconds
  We have a Vocabulary that relate these quantities:
  Cycle time(seconds per cycle)
  Clock Rate(cycles per second)
  CPI(cycles per instruction)
  MIPS-million of instructions per second

## Slide 7: Performance
Performance is determined by execution time
Time= seconds/program
Time== X X
Do any other variables equals performance?
  # of cycles to execute programs?
  # of instructions in the program?
  # of cycles per second?
  Average # of cycles per instructions?
  Average # of instructions per second?
Common mistake thinking one of the variables indicative of performance when it really isn’t.

## Slide 8: CPI Example
Suppose we have two implementations of the same Instruction Set Architecture (ISA).
For some program,
Machine A has clock cycle time 250ps and a CPI of 2.0
Machine B has clock cycle time 500ps and a CPI of 1.2
What machine is faster for this program and by how much??
[Solution - TextBook]

## Slide 9: Basic Equations….
CPU Time=ICxCPIx CCT
CPU Time=ICxCPI/[Clockrate]