## Slide 1: 19CSE211 COMPUTER ARCHITECTURE & ORGANIZATION
Performance Analysis - Problems

## Slide 2: Problem 1
A compiler designer is trying to decide between two code sequences for a particular machine. Based on the hardware implementation, there are three different classes of instructions: Class A, Class B, and Class C, and they require one, two, and three cycles (respectively).
The first code sequence has 5 instructions: 2 of A, 1 of B, and 2 of C The second sequence has 6 instructions: 4 of A, 1 of B, and 1 of C.
Which sequence will be faster? How much? What is the CPI for each sequence?

## Slide 3: Solution
Clock Cycles of M1 = (2 * 1) + ( 2 * 1) + (2 * 3) = 10 cycles
Clock Cycles of M2=(4 * 1)+(1*2)+(1*3) = 9 cycles
M2 is faster than M1 (10/9) = M2 is 1.1 times faster than M1. M1=5x2xCCT, M2=6x1.5xCCT
CPI for each sequence
CPI(M1) = 10/5 = 2
CPI (M2) = 9/6= 1.5

## Slide 4: Problem 2
A given application written in Java runs 15 seconds on a desktop processor. A new Java compiler is released that requires only 0.6 as many instructions as the old compiler. Unfortunately, it increases the CPI (clock cycles per instruction) by 1.1. How fast does the application run using the new compiler ?

## Slide 5: Solution
15 = I (old) *CPI(old)*CCT
x= 0.6 I(old) * CPI(1.1)*CCT
15/x = 1/(0.6*1.1)
x= 15*0.6*1.1
x= 9.9

## Slide 6: Problem 3
Our favorite program runs in 10 seconds on computer A, which has a 400 Mhz. clock. We are trying to help a computer designer build a new machine B, that will run this program in 6 seconds. The designer can use new (or perhaps more expensive) technology to substantially increase the clock rate, but has informed us that this increase will affect the rest of the CPU design, causing machine B to require 1.2 times as many clock cycles as machine A for the same program. What clock rate should we tell the designer to target?"
Assume the program takes X cycles and the desired rate is Y

## Slide 7: Solution
CPI(B) = 1.2 * CPI (A)
CPU clock cycles = I * CPI
10 Sec = [CPU clock cycles of A for program] / 4 GHz ,
10 = I * CPI(A) / 4 GHz
I * CPI (A) = 40 * 10 to the power 9 cycles.
6 Sec = (CPU clock cycles of B for program ] / CR (B)
6=I * CPI(A)*1.2 / CR(B)
CR(B)=40 * 10 to the power 9 * 1.2 / 6 = 48*10 to the power 9/6
CR(B) = 8 GHz

## Slide 8: Problem 4
Instruction Type | CPI | Frequency | CPI * Frequency
ALU | 1 | 50% | 0.5
Branch | 2 | 20% | 0.4
Load | 2 | 20% | 0.4
Store | 2 | 10% | 0.2
Given this machine , the CPI is the sum of (CPI(i) * frequency(i))
Average CPI is 0.5+0.4+0.4+0.2 = 1.5
What fraction of the time is spent for data transfers ?

## Slide 9: Solution
Time spent for data transfer instructions = 0.6 / 1.5 = 40%
Time spent for arithmetic and logic operations = 0.5/1.5= 33 % of time
Time spent for branch instructions = 0.4/1.5 = 26 % of time.
Design Principle - Make the common case fast

## Slide 10: Problem 5
Instruction Type | CPI | Frequency | CPI * Frequency | % of time
ALU | 1 | 50% | 0.5 | 23 %
Load | 5 | 20% | 1 | 45%
Store | 3 | 10% | 0.3 | 14%
Branch | 2 | 20% | 0.4 | 18%
Given this machine , the CPI is the sum of (CPI(i) * frequency(i))
Average CPI is 0.5+1+0.3+0.4 = 2.2
How much faster would the machine be if a better data cache reduced the average load time to 2 cycles?

## Slide 11: Solution
Instruction Type | CPI | Frequency | CPI * Frequency | % of time
ALU | 1 | 50% | 0.5 | 
Load | 2 | 20% | 0.4 | 
Store | 3 | 10% | 0.3 | 
Branch | 2 | 20% | 0.4 | 
Average CPI is 0.5+0.4+0.3+0.4 = 1.6
Relative performance is 2.2 / 1.6 = 1.38