## Slide 1: 19CSE211 COMPUTER ARCHITECTURE & ORGANIZATION
Performance Analysis – Problems(Part II)

## Slide 2: Problem 6
Two different compilers are being tested for a 4 GHz. machine with three different classes of instructions: Class A, Class B, and Class C, which require one, two, and three cycles per instruction (respectively). Both compilers are used to produce code for a large piece of software.
The first compiler's code uses 5 billion Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
The second compiler's code uses 10 billion Class A instructions, 1 billion Class B instructions, and 1 billion Class C instructions.
Which sequence will be faster according to MIPS?
Which sequence will be faster according to execution time?

## Slide 3: Solution
Number of cycles for first compiler’s code = 10 X 109
Number of cycles for second compiler’s code = 15 X 109
Time1 = Cycles per program1/clock rate = (10 X 109) / (4 x 109)
= 2.5 Sec
Time2 = Cycles per program2/clock rate = (15 X 109) / (4 x 109)
= 3.75 Sec

## Slide 4: Solution Contd….
MIPS1 = Instructions / Second
= Instructions / Second
= 7 X 109/ 2.5
= 7 X 103
= 2800
MIPS2 = Instructions / Second
= Instructions / Second
= 12 X 103/ 3.75
= 3200

## Slide 5: Pblm7
Two different compilers are being tested for a 100 MHz. machine with three different classes of instructions: Class A, Class B, and Class C, which require one, two, and three cycles (respectively). Both compilers are used to produce code for a large piece of software. The first compiler's code uses 5 million Class A instructions, 1 million Class B instructions, and 1 million Class C instructions. The second compiler's code uses 10 million Class A instructions, 1 million Class B instructions, and 1 million Class C instructions.
Which sequence will be faster according to MIPS?
Which sequence will be faster according to execution time?

## Slide 6: Solution
A:
EXEC = (5+2+3)/100 = 10/100sec =.1
MIPS = 700/10 = 70
B:
EXEC = (10+2+3)/100 = 15/100sec =.15
MIPS = 1200/15 = 80

## Slide 7: Problem 8
A certain program needs 6000 cycles, and the clock is running at 200MHz. How long will it take to complete the program?
Ans :
Time for program = cycles the program needs*second/cycle
= 6000*1/200 x 106=30s

## Slide 8: Problem 9
CPU clock rate is 1 MHz , program takes 45 million cycles to execute. What’s the CPU time?
Ans
45,000,000 * (1 / 1,000,000) = 45 seconds

## Slide 9: Problem 10
CPU clock rate is 500 MHz , program takes 45 million cycles to execute. What’s the CPU time?
Ans
45,000,000 * (1 / 500,000,000) = 0.09 seconds

## Slide 10: Problem 11
Assume that a benchmark has 100 instructions:
25 instructions are loads/stores (each take 2 cycles)
50 instructions are adds (each takes 1 cycle)
25 instructions are square root (each takes 50 cycles) .
What is the CPI for this benchmark?
Ans
CPI = ((0.25 * 2) + (0.50 * 1) + (0.25 * 50)) = 13.5
(25/100)X2+ (50/100)X1+(25/100)x50