## Slide 1: 19CSE301 COMPUTER ARCHITECTURE & ORGANIZATION
MIPS-PIPELINED ARCHITECTURE

## Slide 2: How can we make a Machine faster?
Solution is Pipelining
Key to all Modern Processors
Performance Equation: CPU Time=CPI x CCT x IC
Under ideal conditions and with large number of instructions, the speedup from Pipelining is approximately equal to the number of stages.

## Slide 3: The five stages of ‘lw’ instruction
IFetch-Fetch the Instruction and Update the PC.
IDecode-Register Fetch and Instruction decode
ALU Execution-Execute R-type; Calculate Memory Address
Memory-Read/Write the data to or from the Data Memory
WBack-Write the Result data in to Register file

## Slide 4: Total Time Calculated for each Instruction from time of each component

## Slide 5: A Pipelined MIPS Processor
Starts the next Instruction before the current one has been completed.
Improves throughput-total amount of work done in a given time.
Instruction Latency is not reduced.
lw
sw
R- Type
Clock cycle(pipeline stage time) is determined or limited by the slowest stage
Speed Up=[800xN]/[800+200xN]

## Slide 6: Single Cycle vs Pipelined Performance
lw
sw
R-Type
Pipelined Implementation(CC=200ps)
To complete an entire instruction in pipelined case takes 1000ps (as compared to 800ps for the single cycle case)
How long does it take to complete 1,000,000 adds?

## Slide 7: Pipelining in MIPS ISA
All Instructions are of same length-can fetch in the Ist stage, decode in the 2nd stage.
Only 3 Instruction formats with symmetry across formats.
Memory operations occur only in loads and stores.
Each Instruction writes at most one result(ie changes the machine state) and writes the result in last stages of pipeline(MEM/WB)
Operands must be aligned in memory so a single data transfer takes only one data memory access.