## Slide 1: 19CSE211 Computer Architecture & Organization
Arithmetic for Computers – Part 1

## Slide 2: Multiplication
Start with long-multiplication approach
multiplicand
multiplier
product
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
Partial products

## Slide 3: The first multiplication algorithm – Sequential Algorithm

## Slide 4: Multiplication hardware – Sequential Algorithm
Figure 3.5

## Slide 5: EXAMPLE : A Multiply Algorithm
Using 4-bit numbers to save space, multiply 2ten × 3ten, or 0010two × 0011two. Figure 3.7 shows the value of each register for each of the steps labeled according to Figure 3.5, with the final value of 0000 0110two or 6ten. Color is used to indicate the register values that change on that step, and the bit circled is the one examined to determine the operation of the next step.

## Slide 6: Multiply example

## Slide 7: MULTIPLY HARDWARE
32-bit Multiplicand reg, 32 -bit ALU, 64-bit Product reg, (0-bit Multiplier reg)
Product
(Multiplier)
Multiplicand
32-bit ALU
Write
Control
32 bits
64 bits
Shift Right

## Slide 8: Multiply Algorithm – Refined algorithm
Done
Yes: 32 repetitions
2. Shift the Product register right 1 bit.
No: < 32 repetitions
1.
Test
Product0
Product0 = 0
Product0 = 1
1a. Add multiplicand to the left half of product &
place the result in the left half of Product register
32nd
repetition?
Start
0000 0011 0010
1: 0010 0011 0010
2: 0001 0001 0010
1: 0011 0000 0010
2: 0001 1000 0010
1: 0001 1000 0010
2: 0000 1100 0010
1: 0000 1100 0010
2: 0000 0110 0010
0000 0110 0010
Product Multiplicand
Notes: Mcand: 0010 P: 0000 0011
1a. 1=>P=P+Mcand Mcand: 0010 P: 0010 0011
2. Shr P Mcand: 0010 P: 0001 0001
1a. 1=>P=P+Mcand Mcand: 0010 P: 0011 0001
2. Shr P Mcand: 0010 P: 0001 1000
1. 0=>nop Mcand: 0010 P: 0001 1000
2. Shr P Mcand: 0010 P: 0000 1100
1. 0=>nop Mcand: 0010 P: 0000 1100
2. Shr P Mcand: 0010 P: 0000 0110

## Slide 9: Multiply in MIPS
Product stored in two 32 bit registers called Hi and Low.
mult $s0,$s1
multu $s0,$s1
Results are moved from Hi/Low .
mfhi $t0 # $t0=Hi
mflo $t1 # $t1 = Low
Pseudo Instruction
mul $t0,$s0,$s1 # $t0 = $s0 * $s1