## Slide 1: 19CSE211-Computer Organization & Architecture - Conversion from MIPS Instruction to Machine Language Format

## Slide 2: Immediate Format
Opcode - 6 bits for indicating the operation,
rs - 5 bits for indicating only one source operand,
rt – 5 bits for indication only one destination operand,
Immediate – 16 bit value data content or 16 bit address.

## Slide 3: I-format Instructions
addi-add immediate,
slti : - set less than immediate,
bne/beq: - conditional branching statements,
Data Transfer Instructions like loads and stores
Constant data specified in an instruction
addi $s3, $s3, 4
I-Format versions: compare register and constant, put result into 2nd register
Set less than immediate
slti rd, rs, imm : if rs<imm set rd=1 else set rd=0

## Slide 4: Immediate instructions
bne/beq : branch on not equal / branch on equal
  beq register1,register2,L1
  bne register1,register2,L1
No subtract immediate instruction
Just use a negative constant
addi $s2, $s1, -1

## Slide 5: addi-Add Immediate
Binary Pattern Representation - 001000 10010 10001 0000000001100100
Machine Language Representation in Hexa Decimal: (22540064)16
Opcode for addi-8, rs-s2 Register(18), rt-s1 Register(17), Immediate value-100
The 32 bit content in s2 Register is added with 100 (represented also as 32-bit)and stored in s1 Register.

## Slide 6: Revision
addi $t0, $t0, 4
Find the machine language representation in hexa-decimal representation corresponding to the above MIPS Instruction
Machine Language Representation in HexaDecimal:( )16

## Slide 7: Set Less than Immediate
slti $t0, $s2, 15 #$t0 = 1 if $s2<15
If the 32-bit content in s2 Register is less than 15, then set it to 1 else 0
Machine format (I format):
Binary Pattern Representation - 001010 10010 01000 0000000000001111
Machine Language Representation in HexaDecimal:(2A48000F)16